## Slide 1: Networking Basics
Week 6
Types of Addresses in IPv4 Networks
Part 2 of 2
Yvan Perron
CST8103 - Fall 2012

## Slide 2: Topics
Quick review of the three address types
Calculating the three address types – complex case
Examples –complex case

## Slide 3: Network Address Types
Network (first address in a network’s address range) and broadcast (last address in a network’s address range) IP addresses are never ever assigned to devices.
Difference between a host and a broadcast address?
    A host address is an address we assign to network devices like computers, printers, servers, laptops, etc. Every (almost!) device needs an IP address in order to communicate.
    A broadcast address is a special address (never, ever assigned to a host). When a network device like a computer, etc wants to send a message to ALL devices in the same network, they send to the broadcast address. The broadcast is a quick and efficient way of sending a network communication to ALL devices of the same network segment.

## Slide 4: Calculations
Perform calculations for 172.16.10.254/16
  Network address (all host bits are 0s)
  Broadcast address (all host bits are 1s)
  Host addresses
    Range  Network +1 to Broadcast -1
    Number of hosts in network = 2^h-2

## Slide 5: Complex Case
Perform calculations for 192.168.1.100/25
  Network address (all host bits are 0s)
  Broadcast address (all host bits are 1s)
  Host addresses
    Range  Network +1 to Broadcast -1
    Number of hosts in network = 2^h-2

## Slide 6: Complex Case Procedure
Steps for calculating the three address types:
  Convert IP address to 32 bit binary
  Draw a vertical line after the last network bit
  Set all host bits to 0s
  Convert 32 bit binary to dotted decimal
    You have your network ID
  Set all host bits to 1s
  Convert 32 bit binary to dotted decimal
    You have your broadcast address
  Add 1 to your network address
    You have your first host address
  Subtract 1 from your broadcast address
    You have your last host address
  Number of hosts in network = 2^h-2

## Slide 7: Complex Case Example
192.168.1.100/25
  11000000101010000000000101100100
  1100000010101000000000010
  1100000010101000000000010

## Slide 8: Complex Case Example
192.168.1.128/25
  11000000101010000000000110000000
  1100000010101000000000011
  1100000010101000000000011

## Slide 9: Summary
Addresses that have subnet masks that are portions of an octet require a more complex procedure in order to calculate the three address types of any IPv4 network segment.

## Slide 10: Next
Practice Tests on Blackboard
Basics of sub netting