## Slide 1: Networking Basics
Week 7
Summary
Address Types and Basic Subnetting
Yvan Perron
CST8103 - Fall 2012

## Slide 2: Topics
Calculating the three Address Types
Basic subnetting

## Slide 3: Address Types
There are three types of addresses within the address range of every network segment:
  Network, host and broadcast
    Network Id
      All host bits are 0s
    Broadcast address
      All host bits are 1s
    Host addresses
      network + 1 to broadcast -1
    Maximum number of hosts in network
      2^h-2
    Remember, the network portion is identical for ALL addresses of same network segment

## Slide 4: 192.168.15.0/24

## Slide 5: Subnetting
Creating multiple networks from a single address block.
Subnetting was necessary as we were running out of address blocks that could be allocated to organizations.
We had to abandon the old classful addressing scheme.

## Slide 6: Subnetting - Illustrated
Subnetting process illustrated
  Start with the mask of our base IP address
11111111111111111111111100000000
      n=24 h=8
  Transform host bits into network bits – our new mask
11111111111111111111111111110000
  Result of subnetting
      b=4 n=24 New h=?
      32=b+n+h
      h=32-(b+n)
      Subnets = 2^b
      Hosts per subnet = 2^h-2

## Slide 7: Subnetting Formulas
Formulas and variables
  h=number of host bits (after borrowing)
  b=number of host bits transformed into network bits (aka borrowed bits)
  n=number network bits (base mask)
  h+n+b=32
  Number of new networks resulting from the subnetting:
    2^b
  Number of hosts per new network
    2^h-2

## Slide 8: End