## Slide 1: Networking Basics
Week 6
Types of Addresses in IPv4 Networks
Part 1 of 2
Yvan Perron
CST8103 - Fall 2012

## Slide 2: Topics
Address types in an IPv4 network
Calculating the address types
Simple Examples

## Slide 3: Network Address Types
Within the address range of every IPv4 network segment with have three address types:
  Network address (Aka the Network Id)
  Host addresses
  Broadcast address

## Slide 4: Network Address Types
Network address
  The address by which we refer to the network segment (like the area code). All addresses in a network have the same network address bits (same area code within the same region).
Host address
  The addresses assigned to hosts in the network segment. Each host has a unique address.
Broadcast address
  A special address used to send data to all hosts in the network segment.
Notes: Network address : is like a are code all the address in a network have the same network address bits. All hosts bits are 0
  Host address : segment assigned to hosts in the network segment: Network +1 to Broadcast -1 number of hosts in network : 2^h-2
Broadcast address: special address used to send data to all hosts in network segment. All host bits are 1
One in broadcast address represented by 255
Only change the last bits for calculation

## Slide 5: Addressing
Network address: 172.16.1.0/24 (same for everyone)
Host addresses: 172.16.1.1/24 to 172.16.1.254/24 (for each hosts (computer))
Broadcast address: 172.16.1.255/24
Network address: 172.16.2.0/24 (same for everyone)
Host addresses: 172.16.2.1 /24 to 172.16.2.254/24 (
For each hosts )
Broadcast address: 172.16.2.255/24

## Slide 6: Calculations
Network address
  All host bits are 0s
Broadcast address
  All host bits are 1s
Host addresses
  Network +1 to Broadcast -1
  Number of hosts in network = 2^h-2
    Where h equals the number of host bits
    Remember: Network bits are constant for all addresses of the same network

## Slide 7: Calculations
Perform calculations for 192.168.15.100/24
  Network address (all host bits are 0s)
    192.168.15.0
  Broadcast address (all host bits are 1s)
    192.168.15.255
  Host addresses
    Range  Network +1 to Broadcast -1
      192.168.15.1 to 192.168.15.255
    Number of hosts in network = 2^h-2
      2^8-2=254 host addresses

## Slide 8: Calculations
Perform calculations for 172.16.10.254/24
  Network address (all host bits are 0s)
  Broadcast address (all host bits are 1s)
  Host addresses
    Range  Network +1 to Broadcast -1
    Number of hosts in network = 2^h-2

## Slide 9: Addressing

## Slide 10: Summary
IPv4 Network Addresses
  Three types
    Network, host and broadcast
  Network address all host bits are 0s
  Broadcast address all host bits are 1s
  Host addresses range between the network and broadcast address
  Remember, the network portion is constant across addresses of same network segment

## Slide 11: Next
Part 2 of 2 – complex examples